## Slide 1
Design and Verification of a
2-Way Set-Associative Cache Controller
Verilog RTL Project
2-Way Set Associative • LRU • Write-Through • No-Write-Allocate
CPU Interface
Cache
Controller
Cache Store

## Slide 2
Project Objective & Scope
Assigned cache configuration
Cache Controller | Verilog RTL | 2/12
Goal
Design and verify a modular Verilog cache controller that demonstrates hit/miss detection, LRU replacement, Write-Through behavior, and No-Write-Allocate handling.
Directed simulation only
Clear PASS/FAIL reporting
Simple main memory; FSM only in cache controller
Implemented Parameters
Address width
16 bits
Cache lines
8 total
Organization
4 sets × 2 ways
Data per line
32 bits
Replacement
LRU
Write policy
Write-Through
Write miss
No-Write-Allocate

## Slide 3
Cache Organization
Address mapping and storage
Cache Controller | Verilog RTL | 3/12
Address Breakdown
TAG [15:2]
14 bits
INDEX
[1:0]
Hit condition: valid way + matching tag
4 sets × 2 ways
Set 0
Way 0
Tag | Data | V
Way 1
Tag | Data | V
Set 1
Way 0
Tag | Data | V
Way 1
Tag | Data | V
Set 2
Way 0
Tag | Data | V
Way 1
Tag | Data | V
Set 3
Way 0
Tag | Data | V
Way 1
Tag | Data | V
1 LRU bit per set
selects replacement victim
No dirty bit
Write-Through policy

## Slide 4
Overall Architecture
Top-level data/control flow
Cache Controller | Verilog RTL | 4/12
Testbench → CPU model → cache controller → main memory

## Slide 5
Module Breakdown
What each file does
Cache Controller | Verilog RTL | 5/12
cpu_model.v
CPU-side adapter
request_sent flag
one cache_req pulse
cache_controller.v
Core cache logic
hit/miss + LRU
4-state FSM
main_memory.v
Backing memory
combinational read
synchronous write
cache_system_top.v
Integration module
connects internal signals
Design decision
Cache controller is the only FSM
Main memory stays simple
Testbench uses read_test() and write_test() tasks
Synthesizable RTL modules:
cpu_model.v, cache_controller.v, main_memory.v, cache_system_top.v

## Slide 6
Cache Controller FSM
Four-state control flow
Cache Controller | Verilog RTL | 6/12
State roles
IDLE: wait for request
LOOKUP: compare both ways
MEM_READ: service read miss
MEM_WRITE: write-through to memory
Write hit and miss both use MEM_WRITE
Only read miss allocates cache line

## Slide 7
Read Operation
Hit vs miss behavior
Cache Controller | Verilog RTL | 7/12
READ HIT
READ MISS
Tag matches
valid way
Cache data
returned to CPU
Update LRU
No memory read
No valid tag
match
Enter MEM_READ
mem_req=1, mem_we=0
Fill invalid way
or replace LRU
Return memory data
to CPU
Key check: read hit must produce Memory Read = 0
Key check: read miss must produce Memory Read = 1

## Slide 8
Write Policy
Write-Through + No-Write-Allocate
Cache Controller | Verilog RTL | 8/12
Same MEM_WRITE state, different cache action before it.
WRITE HIT
WRITE MISS
Address found in cache
Update cached copy
Update LRU
Enter MEM_WRITE
Main memory updated
Address not cached
Do not update cache
No cache allocation
Enter MEM_WRITE
Main memory updated
CPU never writes memory directly — cache controller forwards mem_addr and mem_wdata.

## Slide 9
LRU Replacement Example
Set 0 pressure test
Cache Controller | Verilog RTL | 9/12
Addresses 0x1000, 0x2000, and 0x3000 all map to Set 0.
Read 0x1000
MISS
Way filled
Read 0x2000
MISS
Second way filled
Read 0x1000
HIT
0x1000 becomes MRU
Read 0x3000
MISS
Replace LRU = 0x2000
Read 0x2000
MISS
Eviction confirmed
What this proves
Both ways are used before replacement
LRU metadata changes on a hit
Full set replaces least recently used line
2-way cache needs only one LRU bit per set

## Slide 10
Verification Strategy
Directed tests with compact reporting
Cache Controller | Verilog RTL | 10/12
The testbench focuses on observable behavior, not random coverage.
Read tests
miss → hit
multiple hits
read-after-write
LRU tests
second-way fill
hit updates LRU
evicted line misses
Write tests
write hit
multiple write hits
write-through
Miss policy
write miss
no allocation
read after miss
Memory access counters prove:
Read hit → 0 memory reads
Read miss → 1 memory read
Every write → 1 memory write

## Slide 11
Simulation Evidence
EPWave and console summary
Cache Controller | Verilog RTL | 11/12
EPWave shows CPU requests, cache request/ready behavior, memory transactions, returned data, and FSM state transitions.
15 / 15 directed tests passed
FSM states visible: IDLE, LOOKUP, MEM_READ, MEM_WRITE

## Slide 12
Conclusion
What the project demonstrates
Cache Controller | Verilog RTL | 12/12
Implemented successfully
2-way set-associative cache controller in Verilog
LRU replacement verified using Set-0 pressure tests
Write-Through verified on write hits and write misses
No-Write-Allocate verified by read-after-write-miss behavior
Final Check
15 directed tests
0 failed checks
Synthesizable RTL design
Ready for project review and waveform explanation